## Slide 1: Tentative Title: Integrative Trajectory Forecasting for Autonomous Vehicles in Mixed Traffic Environments
Supervised By:
Md Rakibul Haque
Lecturer,
Dept. of Computer Science & Engineering, RUET.
Presented By:
Md. Nazmul Hossain ID : 1803170
Department of Computer Science & Engineering

## Slide 2
Topic Outline
Introduction
Literature Review
Challenges
Objectives
Methodology
Dataset Details
Results
Conclusion
Future Work
References

## Slide 3
Introduction
Trajectory refers to a path that a vehicle moves through space over time.
For of an autonomous vehicle, trajectory not only the route but also it’s motion—speed, acceleration, and direction etc.
Fig – 1: Some Trajectories of Various Vehicle [5].

## Slide 4
Introduction (CONT’D)
Mixed traffic environment consists of different types of road users, such as pedestrians, bicycles, motorcycles, cars, and buses, share the same space and interact with each other.
Fig – 2: Mixed Traffic Environment [1].

## Slide 5
Literature Review
TrafficPredict: Trajectory Prediction for Heterogeneous Traffic-Agents [2]
Performances:
Using previous state-of-the-art approaches in accuracy for trajectory prediction in heterogeneous traffic
Offer real-time performance without assumptions about traffic conditions or the number of agents.
Limitations:
The accuracy varies with traffic conditions and the historical data available.
Future improvements will consider additional constraints such as lane directions, traffic signals, and rules.

## Slide 6
Literature Review (CONT’D)
Interactive Trajectory Prediction for Autonomous Driving via
Recurrent Meta Program Induction Network [3]
Performances :
Use traditional kernel methods in predicting the trajectory of human-driven cars, achieving lower mean error rates in trajectory prediction for both longitudinal and lateral directions.
Limitations:
Future developments are needed for a more advanced generator and observer structure to further reduce prediction errors and to extend the framework to more general scenarios, such as turns at intersections and highway merging.

## Slide 7
Literature Review (CONT’D)
Probabilistic Trajectory Prediction for Autonomous Vehicles with Attentive Recurrent Neural Process [4]
Performances :
The Attentive Recurrent Neural Process (ARNP) proposed in the paper effectively captures sequential information traffic scenarios.
ARNP outperforms several previous approaches in terms of prediction accuracy, variance, and probability expressiveness by predicting an explicit distribution.
Limitations:
Future developments are needed for better recognize and adapt to poorly understood traffic.

## Slide 8
Challenges
Work on Urban Areas Consists of Mixed Traffics
Considering Driver Dynamic Behavior and Turning Radius
Reduce Prediction Error

## Slide 9
Objectives
  Deals with mixed traffic environment consists of various cars, bicycles, bikes, buses, pedestrians, traffic lights etc. in an urban areas.
  Considering driver dynamic behavior and turning radius.
  Also increasing the accuracy of the model is an obligatory part of my work.

## Slide 10
Methodology

## Slide 11
Methodology (CONT’D)

## Slide 12
Methodology (CONT’D)
Fig – 3: (a) S

## Slide 13
Methodology (CONT’D)
Instance & Category Layer

## Slide 14
Methodology (CONT’D)
Two Maps
LSTM
Output
LSTM
Conv1
Conv2
Conv1
Conv2
LSTM
Conv1
Conv2
+
LSTM
Ego Agent
Horizon Map
Neighbor Map
Fig – 4: LSTM-CNN Architecture

## Slide 15
Dataset Details
Attribute | Description
Frame_id | It indicates a unique frame of a video stream which is captured on 2fps rate.
Object_id | It indicates the unique object.
Object_type | It indicates the type of an object such as vehicle, bicycle, pedestrian or other.
Position_x,y,z | The position x,y,z indicates the location of an object in world coordinate system.
Object_length | It indicates the length of an object.
Object_width | It indicates the width of an object.
Object_height | It indicates the height of an object.
Heading | The heading value is the steering radian with respect to the direction of the object.
[5]
Dataset Name: ApolloScape Dataset
It contains 53 file, each file for 1 min sequence with 2 fps (frame per second) rate.

## Slide 16
Dataset Details
Attribute | Description
Frame_id | It indicates a unique frame of a video stream which is captured on 2fps rate.
Num_agent | It indicates the number of agents of this frame.
Position_x,y | The position x,y indicates the ground truth value of an agent in world coordinate system.
Agent_length | It indicates the length of an agent.
Agent_width | It indicates the width of an agent.
Agent_name_id | It indicates the type of an agent with an id.
[6]
Dataset Name: TRAF Dataset

## Slide 17
Dataset Details
Dataset Name: NGSIM (Next Generation Simulation) Dataset

## Slide 18
Results
I implement the model with the NGSIM Dataset –
Average Displacement Error (ADE) | 2.86164
Final Displacement Error (FDE) | 5.19008
Operation | Value (s)
Data Loading Time | 0.418
Training Time | 30961.05
Testing Time | 119.77

## Slide 19
Results
Average Training Loss vs Epoch Curve –

## Slide 20
4/27/2024
Integrative Trajectory Forecasting for Autonomous Vehicles in Mixed Traffic Environments
20
Results
Average Validating Loss vs Epoch Curve –

## Slide 21
Results
Model | ADE | FDE
RNN-ED | 6.86 | 10.02
S-LSTM | 5.73 | 9.58
S-GAN | 5.16 | 9.42
CS-LSTM | 7.25 | 10.05
TraPHic | 5.63 | 9.91
Our Model | 2.86 | 5.19

## Slide 22
Conclusion
In conclusion, we have successfully implemented the existing model and evaluated the results. However, we have identified certain limitations in the existing approach, including the absence of considerations for dynamic motion, turning radius, and driver behavior. To address these shortcomings and enhance the model's capabilities, our proposed model incorporates these crucial characteristics, paving the way for a more comprehensive and accurate solution.

## Slide 23
Future Work
Apply the Hybrid Model on another Dataset and Observe the result
Combine the prediction result of all existing traffic agent and try to give suggestion our vehicle trajectory

## Slide 24
References
[1] https://c8.alamy.com/comp/2GDM3KX/isometric-city-crossroad-with-cars-road-intersection-traffic-jam-urban-downtown-street-with-transport-and-people-vector-illustration-public-and-private-transport-in-residential-area-2GDM3KX.jpg
[2] Yuexin Ma, Xinge Zhu, Sibo Zhang, Ruigang Yang, Wenping Wang, Dinesh Manocha4
[3] Chiyu Dong, Yilun Chen and John M. Dolan
[4] Jiacheng Zhu, Shenghao Qin, Wenshuo Wang, Member, IEEE, and Ding Zhao
[5] https://apolloscape.auto/trajectory.html
[6] https://gamma.umd.edu/researchdirections/autonomousdriving/trafdataset

## Slide 25
Thank You

## Slide 26
Q/A